Five level cascaded h-bridge multilevel inverter using multicarrier pulse width modulation technique

ABSTRACT

The multilevel inverter utilization has been increased since the last decade. These new type of inverters are suitable in various high voltage and high power applications due to their ability to synthesize waveforms with better harmonic spectrum and faithful output. This paper presents an asymmetrical five level cascaded H-bridge multilevel inverter, using multicarrier pulse width modulation technique. And also comparison is made between multicarrier pulse width modulation and the embedded matlab function.

The multilevel inverter has been implemented in various applications ranging from medium to high-power levels, such as motor drives, power conditioning devices, also conventional or renewable energy generation and distribution. The different multilevel inverter structures are cascaded H-bridge, diode clamped and flying capacitor multilevel inverter. Among the three topologies, the cascaded multilevel inverter has the potential to be the most reliable and achieve the best fault tolerance owing to its modularity, a feature that enables the inverter to continue operating at lower power levels after cell failure. Modularity also permits the cascaded multilevel inverter to be stacked easily for high power and high-voltage applications.

In this paper a new topology with reduced number of switches and also the cost. From the results, the proposed inverter provides higher output quality with relatively lower power loss as compared to the other conventional inverters with the same output quality The Simulation results are presented to prove that THD is reduced with the multicarrier modulation..

Block diagram for proposed system

DESIGNG SOFTWARE AND TOOLS:

MAT LAB /SIMULATION Software and sim power systems tools are used. Mainly control system tools, power electronics and electrical elements tools are used.