# POWER FAILURE ALART SYSTEM

AIM:

The aim of the project is design system for a power supply monitoring device that will trigger a buzzer when the mains supply cuts off.

BLOCK DIAGRAM:

PowerSUPPLY:

DESCRIPTION:

This power failure alarm project is a power supply monitoring device that will trigger a buzzer when the mains supply cuts off. At the same time, the light emitting diode will be turned ON. This device is helpful to inform the loss of power supply to some critical installation such as a pump in a fish tank. Once the buzzer sound, you will know that there is a loss of power supply and actions need to be taken to rectify the situation by providing alternative power supply or relocating the installation.

The circuit shown below consists of a AC relay. If the mains input is 120V AC, use a 120V AC relay. If the mains input is 240V AC, use a 240V AC relay. The relay is a Single Pole Double Throw (SPDT) type where the COM will be connected to NC terminal if it is not energized  Once energized, the COM terminal will be connected to the NO terminal.

This type of relay is commonly available from any electronics shop. Make sure that the coil of the relay rating is rated according to your mains power supply. Improper rating will cause damage to the relay or the relay will simply not work even though it is connected properly to the mains supply. Be extra careful when you connect the mains to the relay. Make sure that you take the necessary precaution such as isolating the mains before connecting the relay.

When the mains power supply is available, the relay will be energized and the COM contact will be connected to the NO terminal thus disconnecting the 9V power supply in the circuit. When the mains supply cuts off, the COM will be connected to NC terminal and buzzer will sound. LED will light up. Switch S1 is used to enable or disable the buzzer and LED in the circuit.

HARDWARE:

- RELAY

- LED

- BUZZER

- SWITCH

- POWER SUPPLY

RESULT:

Hence by the project is design system for a power supply monitoring device that will trigger a buzzer when the mains supply cuts off.

# Text boxes

POWER SUPPLY

Regulator         section

Filter

Circuit

Bridge

Rectifier

Step Down

Transformer

RELAY

BUZZER

SWITCH

LED