TEMPERATURE BASSED MOTOR CONTROL

AIM:

The main aim of the project is to controlling of a MOTOR, bassed on temperature sensore.

PURPOSE:

The purpose of the project is MOTOR controlling without human effort, this will controlled by temperature sensor.

BLOCK DIAGRAM:

POWER SUPPLY:

DESCRIPTION:

A motor is an electromechanical device, which converts electrical pulse into discrete mechanical movement. The shaft or spindle of motor is incremented in discrete steps when electrical command pulse is applied to it in the proper sequence.

The circuit exploits the property of Thermistor to operate the DC Fan. Thermistor is a kind of temperature dependent resistor and its resistance varies depending on the temperature in its vicinity. There are two types of Thermistors- NTC and PTC.

Negative temperature coefficient (NTC) Thermistor decreases its resistance when the temperature increases while Positive temperature coefficient (PTC) increases its resistance when the temperature increases. Thermistors are bead like resistors available from 100 ohms to 10K or more values. Here a 4.7K NTC Thermistor is used as a voltage comparator to switch on the DC fan.

When the temperature is normal (as set by VR), pin gets higher voltage and makes the output high. This high output keeps T1 off since its base is positive. DC fan remains off in this condition. When the temperature increases above the value set by VR, resistance of Thermister decreases and the voltage at pin decreases. As a result, output becomes low to switch on T1.

A DC Motor turns on to increase the air circulation. When the temperature returns normal, Fan automatically turns off. Diode

1N4007  is necessary to remove back EMF when T1 turns off.

HARDWARE COMPONENTS:

- POWER SUPPLY

- DC MOTOR

- MOTOR DRIVER

- TEMPERATURE SENSORE

APPLICATIONS:

  - INDUSTRIAL MATCHINE COOLING.etc

RESULT:

Hence by using this project we can controlling of the DC MOTOR using  temperature sensore.

# Text boxes

POWER SUPPLY

DRIVER     CIRCUIT

TEMPERATURE SENSORE

MOTOR

Bridge

Rectifier

Step Down

Transformer

Regulator         section

Filter

Circuit