A HIGH PERFORMANCE INDUCTION MOTOR DRIVE SYSTEM USING FUZZY LOGIC CONTROLLER

ABSTRACT

Although induction motors have many advantageous characteristics, they also posse's nonlinear and time-varying dynamic interactions, Using conventional PI controller, it is very difficult and complex to design a high performance induction motor drive system. The fuzzy logic control (FLC) is attractive approach, which can accommodate motor parametric variations and difficulty in obtaining an accurate mathematical model of induction motor due to rotor parametric and load time constant variations. Basically, the motor drive system comprises a voltage source inverter-fed induction motor (VSIM): namely a three-phase voltage source inverter and the induction motor. The squirrel-cage induction motor voltage equations are based on an orthogonal d-q reference-rotating frame where the coordinates rotate with the controlled source frequency.

This project presents a novel fuzzy logic controller for high performance induction motor drive system. The inputs of a squirrel cage induction machine are the three-phase voltages, their fundamental frequency, and the load torque. The outputs, on the other hand, are the three phase currents, the electrical torque, and the rotor speed. The d-q model requires that all the three-phase variables have to be transformed to the two-phase synchronously rotating frame. Consequently, the induction machine model will have blocks transforming the three-phase voltages to the d-q frame and the d-q currents back to three-phase. The inputs to the fuzzy logic controller are the linguistic variables of speed error and change of speed error, while the output is change in switching control frequency of the voltage source inverter.

In this project a comparison between fuzzy logic controller and traditional PI controllers are presented. The FLC does not need exact knowledge of induction motor and tolerate range load excursions and parametric variations. The control assignment rules are obtained using heuristic trial and error and human expertise. Simulink software that comes along with MATLAB was used to simulate the proposed model.