A NOVEL THREE-PHASE TO FIVE-PHASE  TRANSFORMATION USING A SPECIAL TRANSFORMER CONNECTION

ABSTRACT

The first five-phase induction motor drive system was proposed in the late 1970s for adjustable speed drive applications. Since then, a considerable research effort has been in place to develop commercially feasible multiphase drive Systems .Multiphase (more than three phase) systems are the focus of research recently due to their inherent advantages compared to their three-phase counterparts. The multiphase motors are invariably supplied by ac/dc/ac converters.

This is a special transformer connection scheme to obtain a balanced five-phase supply with the input as balanced three phase. The fixed voltage and fixed frequency available grid supply can be transformed to the fixed voltage and fixed frequency five-phase output supply. Since input is a three-phase system, the windings are connected in an usual fashion. Three separate cores are designed with each carrying one primary and three secondary coils, except in one core where only two secondary coils are used. Six terminals of primaries are connected in an appropriate manner resulting in star and/or delta connections and the 16 terminals of secondaries are connected in a different fashion resulting in star or polygon output. The connection scheme of secondary windings to obtain a star output. The turn ratios are different in each phase.

The choice of turn ratio is the key in creating the requisite phase displacement in the output phases. The construction of output phases with requisite phase angles of 72 between each phase is obtained using appropriate turn ratios. The designed transformation turns ratio can be achieved by simply multiplying the gain factor in the turn ratios.

A five-phase induction motor under a loaded condition is used to prove the viability of the transformation system. It is expected that the proposed connection scheme can be used in drives applications and may also be further explored to be utilized in multiphase power transmission systems.