SIMULATION OF DISTRIBUTED POWER-FLOW CONTROLLER (DPFC)

ABSTRACT

This paper describes the steady-state response and control of power in transmission line equipped with FACTS devices. Basically, the family of FACTS devices based on voltage source converters (VSCs) consists of a series compensator, a shunt compensator, and a shunt/series compensator. The static Compensator (STATCOM) is a shunt connected device that is able to provide reactive power support at a network location far away from the generators. Through this reactive power injection, the STATCOM can regulate the voltage at the connection node. The static synchronous series compensator (SSSC) is a series device which injects a voltage in series with the transmission line.

The Unified Power Flow Controller (UPFC) is comprised of a STATCOM and a SSSC, coupled via a common DC link to allow bi-directional flow of active power between the series output terminals of the SSSC and the shunt output terminals of the STATCOM. Each converter can independently generate (or) absorb reactive power at its own AC terminal. The two converters are operated from a DC link provided by a DC storage capacitor.

The UPFC is not widely applied in practice, due to their high cost and the susceptibility to failures. Generally, the reliability can be improved by reducing the number of components; however, this is not possible due to the complex topology of the UPFC.  The same as the UPFC, the DPFC is able to control all system parameters like line impedance, transmission angle and bus voltage.

In this paper detailed simulations are carried out on two-machine systems to illustrate the control features of these devices and their influence to increase power transfer capability and improve system reliability. The DPFC is derived from the unified power-flow controller (UPFC) and DPFC has the same control capability as the UPFC. The DPFC can be considered as a UPFC with an eliminated common dc link. The active power exchange between the shunt and series converters, which is through the common dc link in the UPFC, is now through the transmission lines at the third-harmonic frequency. The interaction between the DPFC, the network and the machines are analyzed.