AN ENHANCED MICROGRID LOAD DEMAND SHARING STRATEGY

ABSTRACT

For the operation of autonomous microgrids, an important task is to share the load demand using multiple distributed generation (DG) units. In order to realize satisfied power sharing without the communication between DG units, the voltage droop control and its different variations have been reported. However, in a low-voltage microgrid, due to the effects of nontrivial feeder impedance, the conventional droop control is subject to the real and reactive power coupling and steady-state reactive power sharing errors.

Furthermore, complex microgrid configurations (looped or mesh networks) often make the reactive power sharing more challenging. In response to the islanding microgrid control challenges, this paper presents a simple reactive power sharing compensation scheme. With the proposed scheme, reactive power sharing errors are significantly reduced. After the compensation, the proposed droop controller will be automatically switched back to the conventional droop controller. To improve the reactive power sharing accuracy, this paper proposes an enhanced control strategy that estimates the reactive power control error through injecting small real power disturbances, which is activated by the low-bandwidth synchronization signals from the central controller. At the same time, a slow integration term for reactive power sharing error elimination is added to the conventional reactive power droop control.

The proposed compensation method achieves accurate reactive power sharing at the steady state, just like the performance of real power sharing through frequency droop control. Simulation results validate the feasibility of the proposed method using MATLAB.