MULTI MACHINE POWER SYSTEM STABILITY ENHANCEMENT USING STATIC SYNCHRONOUS SERIES COMPENSATOR (SSSC)

ABSTRACT

Increasing demands, lack of long-term planning, and the need to provide open access electricity market for Generating Companies and utility customers, all of them have created tendencies toward less security and reduced quality of supply. The power systems of today, by and large, are mechanically controlled. A problem with mechanical devices is that control cannot be initiated frequently, because these mechanical devices tend to wear out very quickly compared to static devices. Flexible AC Transmission Systems devices could be a means to carry out this function without the drawbacks of the electromechanical devices such as slowness and wear. The static synchronous series compensator (SSSC) FACTS controller is used to prove its performance in terms of stability improvement.

This paper investigates the enhancement of voltage stability using Static Synchronous Series Compensator (SSSC). The continuous demand in electric power system network has caused the system to be heavily loaded leading to voltage instability. Under heavy loaded conditions there may be insufficient reactive power causing the voltages to drop. This drop may lead to drops in voltage at various buses.

The result would be the occurrence of voltage collapse which leads to total blackout of the whole system. Flexible AC transmission systems (FACTS) controllers have been mainly used for solving various power system stability control problems. In this study, a static synchronous series compensator (SSSC) is used to investigate the effect of this device in controlling active and reactive powers as well as damping power system oscillations in transient mode. The PI controller is used to tune the circuit and to provide the zero signal error. The dynamic performance of SSSC is presented by real time voltage and current waveforms using MATLAB software for IEEE 4 bus system.