Power Quality Improvement of Grid Interconnected 3-phase 4-wire Distribution System using Fuzzy logic control

ABSTRACT

This paper presents a grid interfacing inverter that compensates power quality problems and it can also interface renewable energy sources with the electric grid. The grid interfacing inverter can effectively be utilized to perform following functions: 1) transfer of active power harvested from the renewable resources; 2) load reactive power demand support; 3) current harmonic compensation at PCC; and 4) current unbalance and neutral current compensation in case of 3-phase 4-wire system.

The ability of fuzzy logic to handle rough and unpredictable real world data made it suitable for a wide variety of applications, especially, when the models or processes are too complex to be analyzed by classical methods. In this paper fuzzy logic controller is used for controlling the DC capacitor voltage.

However, in this paper incorporated the features of APF in the, conventional inverter interfacing renewable with the grid, without any additional hardware cost. That conventional inverter is called as a "grid interfacing inverter". The inverter is controlled to perform as a multifunction device by incorporating active power filter functionality.

Simulations using MATLAB / SIMULINK are carried out to verify the performance of the proposed controller. The results show that the proposed controller has fast dynamic response, high accuracy of tracking the DC-voltage reference, and strong robustness to load parameters variation.