Power Quality Improvement using Fuzzy Logic based UPQC

ABSTRACT

A unified power quality controller (UPQC) using a fuzzy logic controller (FLC) has been proposed. The shunt APFs are used to compensate current related problems, such as reactive power compensation, current harmonic filtering, load unbalance compensation, etc. The series APFs are used to compensate voltage related problems, such as voltage harmonics, voltage sag, voltage swell, voltage flicker, etc. The unified power quality conditioner (UPQC) aims at integrating both shunt and series APFs through a common DC link capacitor.

The UPQC is similar in construction to a unified power flow controller (UPFC). The UPFC is employed in power transmission system, whereas the UPQC is employed in a power distribution system. The primary objective of UPFC is to control the flow of power at, fundamental frequency. On the other hand the UPQC controls distortion due to harmonics and unbalance in voltage in addition to control of flow of power at the fundamental frequency. In this work, the conventional PI controller has been replaced by a fuzzy controller (FC). The FC has been used in APFs in place of conventional PI controller for improving the dynamic performance.

The results obtained through the FLC are good in terms of dynamic response because of the fact that the FLC is based on linguistic variable set theory and does not require a mathematical model of the system. Moreover, the tedious method of tuning the PI controller is not required in case of FLC. Simulations are carried out using MATLAB/Simulink to validate the theoretical findings.