A NEW APPROACH TO MULTIFUNCTIONAL DYNAMIC VOLTAGE RESTORER IMPLEMENTATION FOR EMERGENCY CONTROL IN DISTRIBUTION SYSTEMS

ABSTRACT

The dynamic voltage restorer (DVR) is one of the modern devices used in distribution systems to protect consumers against sudden changes in voltage amplitude. In this project, emergency control in distribution systems is discussed by using the proposed multifunctional DVR control strategy. Also, the multi loop controller using the Posicast and P+Resonant controllers is proposed in order to improve the transient response and eliminate the steady-state error in DVR response, respectively.

The main purpose is to detect and compensate for the voltage sag with minimum DVR active power injection. Also, the in-phase compensation method can be used for sag and swell mitigation. The multiline DVR can be used for eliminating the battery in the DVR structure and controlling more than one line. Moreover, research has been made on using the DVR in medium level voltage. Harmonic mitigation and control of DVR under frequency variations are also in the area of research. The closed-loop control with load voltage and current feedback is introduced as a simple method to control the DVR.

The proposed algorithm is applied to some disturbances in load voltage caused by induction motors starting, and a three-phase short circuit fault. Also, the capability of the proposed DVR has been tested to limit the downstream fault current. The current limitation will restore the point of common coupling (PCC) (the bus to which all feeders under study are connected) voltage and protect the DVR itself. The innovation here is that the DVR acts as a virtual impedance with the main aim of protecting the PCC voltage during downstream fault without any problem in real power injection into the DVR.

The basis of the proposed control strategy in this project is that when the fault current does not pass through the DVR, an outer feedback loop of the load voltage with an inner feedback loop of the filter capacitor current will be used. Also, a feed forward loop will be used to improve the dynamic response of the load voltage. Moreover, to improve the transient response, the Posicast controller and to eliminate the steady-state error. Simulation results show the capability of the DVR.