ENHANCED Power Quality Control Strategy for Single-Phase Inverters in Distributed Generation Systems

Abstract

Power electronic converters are commonly used for interfacing distributed generation (DG) systems to the electrical power network. This project deals with a single-phase inverter for DG systems requiring power quality features, such as harmonic and reactive power compensation for grid-connected operation.

The idea is to integrate the DG unit functions with shunt active power filter capabilities. With this approach, the inverter controls the active power flow from the renewable energy source to the grid and also performs the nonlinear load current harmonic compensation by keeping the grid current almost sinusoidal.

This project deals with a single-phase H-bridge inverter for DG systems, requiring power quality features as harmonic and reactive power compensation for grid-connected operation. The proposed control scheme employs a current reference generator based on SSI and IRP theory, together with a dedicated repetitive current controller.

The grid-connected single-phase H-bridge inverter injects active power into the grid and is able to compensate the local load reactive power and also the local load current harmonics.

Simulation results are carried out and they verify the effectiveness of the proposed approach. Analytical expectations are verified using simulations in the MATLAB/SIMULINK environment, based on a detailed system model.