LOAD COMPENSATION FOR DIESEL GENERATOR BASED ISOLATED GENERATION SYSTEM EMPLOYING DSTATCOM

ABSTRACT

This project presents the control of distribution static synchronous compensator (DSTATCOM) for reactive power, harmonics and unbalanced load current compensation of a diesel generator set for an isolated system. The control of DSTATCOM is achieved using least mean square-based adaptive linear element (Adaline). An Adaline is used to extract balanced positive sequence real fundamental frequency component of the load current and a proportional–integral (PI) controller is used to maintain a constant voltage at the dc-bus of a voltage-source converter (VSC) working as a DSTATCOM. Switching of VSC is achieved by controlling source currents to follow reference currents using hysteresis-based PWM control.

This scheme is simulated under MATLAB environment using Simulink and PSB block-set toolboxes for feeding linear and nonlinear loads. The modeling is performed for a three-phase, three-wire star connected synchronous generator coupled to a diesel engine, along with the three-leg VSC working as a DSTATCOM. Results are presented to verify the effectiveness of the control of DSTATCOM for the load compensation and an optimal operation of the DG set. This project presents a DSTATCOM for the load compensation of a diesel generator set to enhance its performance. The control of DSTATCOM with capabilities of reactive power, harmonics and unbalanced load compensation is achieved by Least Mean Square (LMS) algorithm based adaptive linear element (Adaline).

The Adaline is used to extract positive-sequence fundamental frequency real component of the load current. The dc-bus voltage of voltage source converter (VSC) is supported by a proportional–integral (PI) controller which computes current component to compensate losses in DSTATCOM. The extraction of reference currents using Adaline involves an estimation of weights. These weights are measure of peak of fundamental frequency real current component of the load current. The life of a DG set is enhanced in the absence of unbalanced and harmonic currents. The modeling of the DG set is performed using a synchronous generator, a speed governor, and the excitation control system is simulated under MATLAB environment using Simulink…